Stream Name:									Site code:

Date/Time:									Investigator(s):

Latitude:									Longitude:

Site Description:								Weather conditions:

| Habitat Parameter | Reference | Good | Fair | Poor |
| --- | --- | --- | --- | --- |
| Epifaunal Substrate/Cover | Greater than 70% (50% for low gradient streams) of stream bed and lower banks covered with mix of substrates favorable for epifaunal colonization and fish cover; substrates include snags, submerged logs, undercut banks, and unembedded cobbles and boulders (for high gradient) | 40-70% (30-50% for low gradient streams) of stream bed and lower banks covered with a mix of substrates favorable for epifaunal colonization and fish cover | 20-40% (10-30% for low gradient streams) of stream bed and lower banks covered with substrates favorable for epifaunal colonization and fish cover; few substrate types present | Less than 20% (10% for low gradient streams) of stream bed and lower banks covered with substrates favorable for epifaunal colonization and fish cover; few substrate types present |
|  | 20 19 18 17 16 | 15 14 13 12 11 | 10 9 8 7 6 | 5 4 3 2 1 |
| Embeddedness (high gradient) | Gravel, cobble, and boulder particles are 0-25% surrounded by fine sediment. Layering of cobble provides diversity of niche space. | Gravel, cobble, and boulder particles are 25-50% surrounded by fine sediment. | Gravel, cobble, and boulder particles are 50-75% surrounded by fine sediment. Little open space between particles. | Gravel, cobble, and boulder particles are more than 75% surrounded by fine sediment. Almost no open space between particles. |
|  | 20 19 18 17 16 | 15 14 13 12 11 | 10 9 8 7 6 | 5 4 3 2 1 |
| Pool Substrate Characterization (low gradient) | Characterization (low gradient) Mixture of substrate materials, with gravel and firm sand prevalent; root mats and submerged vegetation common. | Mixture of soft sand, mud, or clay; mud may be dominant; some root mats and submerged vegetation present. | All mud or clay or sand bottom; little or no root mat; no submerged vegetation. | Hard-pan clay or bedrock; no root mat or vegetation. |
|  | 20 19 18 17 16 | 15 14 13 12 11 | 10 9 8 7 6 | 5 4 3 2 1 |
| Velocity/Depth Patterns (high gradient) | All 4 velocity/depth patterns present: slow-deep, slow-shallow, fast-deep, fast-shallow. Slow is < 1 ft/s. (0.3 m/s), deep is > 1.5 ft (0.5 m). | Only 3 of the 4 patterns present (if fast-shallow is missing, score lower than if missing other regimes). | Only 2 of the 4 patterns present (if fast-shallow or slow-shallow are missing, score low). | Dominated by 1 velocity/ depth pattern (usually slow-deep). |
|  | 20 19 18 17 16 | 15 14 13 12 11 | 10 9 8 7 6 | 5 4 3 2 1 |
| Pool Variability (low gradient) | Even mix of large-shallow, large-deep, small-shallow, small-deep pools present. | Majority of pools large-deep; very few shallow. | Shallow pools much more prevalent than deep pools. | Majority of pools small-shallow or pools absent. |
|  | 20 19 18 17 16 | 15 14 13 12 11 | 10 9 8 7 6 | 5 4 3 2 1 |
| Sediment Deposition | Little or no enlargement of mid-channel bars or point bars and < 5% (20% in low gradient streams) of the bottom affected by sediment deposition. | Some new increase in bar formation, mostly from gravel, sand or fine sediment; -30% (20-50% in low gradient streams) of the bottom affected; slight deposition in pools. | Moderate deposition of new gravel, sand or fine sediment on old and new bars; 30-50% (50-80% in low gradient streams) of the bottom affected; sediment deposits at obstructions, constrictions, and bends; moderate deposition of pools prevalent. | Heavy deposits of fine material, increased bar development; > 50% (80% in low gradient streams) of the bottom changing frequently; pools almost absent due to substantial sediment deposition. |
|  | 20 19 18 17 16 | 15 14 13 12 11 | 10 9 8 7 6 | 5 4 3 2 1 |
| Channel Flow Status | Water reaches base of both lower banks, and <10% of channel bed substrate is exposed. | Water fills >75% of the available channel; or <25% of channel bed substrate is exposed. | Water fills 25-75% of the available channel, and/or riffle substrates are mostly exposed. | Very little water in channel and mostly present as standing pools. |
|  | 20 19 18 17 16 | 15 14 13 12 11 | 10 9 8 7 6 | 5 4 3 2 1 |
| Channel Alteration | Channelization in the form of dredging, straightening, berms or streambank armoring absent; stream with natural pattern. | Some channel alterations present along 10-20% of segment, usually in areas of bridge abutments; evidence of past channelization, (greater than past 20 yr) may be present, but recent channelization is not present. | Channelization along 20-80% of stream segment ; riprap or armoring present on both banks. | Over 80% of the stream segment channelized and disrupted. Instream habitat greatly altered or removed entirely. |
|  | 20 19 18 17 16 | 15 14 13 12 11 | 10 9 8 7 6 | 5 4 3 2 1 |
| Frequency of riffles/steps (high gradient) | Occurrence of riffles/steps relatively frequent; ratio of distance between riffles is 5-7 times (steps 3-5 times) stream width; variety of habitat is key. In streams where riffles/steps are continuous, presence of boulders or other large, natural obstruction is important. | Occurrence of riffles/steps infrequent; distance between riffles is 7-15 times (steps 5-15 times) stream width. | Occasional riffle/step or bend; bottom contours provide some habitat; distance between riffles/steps is 15 to 25 stream widths. | Generally all flat water or shallow riffles/steps; poor habitat; distance between riffles/steps is >25 stream widths. Mostly runs. |
|  | 20 19 18 17 16 | 15 14 13 12 11 | 10 9 8 7 6 | 5 4 3 2 1 |
| Channel Sinuosity (low gradient) | The bends in the stream increase the stream length 2.5 to 4 times longer than the straight down-valley length. | The bends in the stream increase the stream length 1.5 to 2.5 times longer than the straight down-valley length. | The bends in the stream increase the stream length 1 to 1.5 times longer than the straight down-valley length. | Channel straight; waterway has been channelized for a long distance. |
|  | 20 19 18 17 16 | 15 14 13 12 11 | 10 9 8 7 6 | 5 4 3 2 1 |
| Bank Stability (score each bank) Note: determine left or right side by facing downstream. | Banks stable; evidence of erosion or bank failure absent or minimal; < 5% of bank affected. | Moderately stable; infrequent, small areas of erosion mostly re-vegetated. 5-30% of bank in segment (or reach) has areas of erosion. | Moderately unstable; 30-60% of bank in segment (or reach) has areas of erosion; high erosion potential from crumbling, unvegetated banks during floods. | Unstable; many eroded areas; "raw" areas frequent along straight sections and bends; obvious bank sloughing; 60-100% of bank has erosional scars. |
| Score ___ (LB) Score ___ (RB) | Left bank 10 9 | 8 7 6 | 5 4 3 | 2 1 0 |
|  | Right bank 10 9 | 8 7 6 | 5 4 3 | 2 1 0 |
| Bank Vegetative (score each bank) Note: determine left or right side by facing downstream. | More than 90% of the streambank surfaces and immediate riparian zone covered by native vegetation, including trees, understory shrubs, or herbaceous vegetation; vegetative disruption through grazing or mowing minimal or not evident; almost all plants allowed to grow naturally. | 70-90% of the streambank surfaces covered by native vegetation, but one class of plants is not well-represented; disruption evident but not affecting full plant growth potential to any great extent; more than one-half of the potential plant stubble height remaining. | 50-70% of the streambank surfaces covered by vegetation; disruption obvious; patches of bare soil or closely cropped vegetation common; less than one-half of the potential plant stubble height remaining. | Less than 50% of the streambank surfaces covered by vegetation; disruption of streambank vegetation is very high; vegetation has been removed to 5 centimeters or less in average stubble height. |
| Score ___ (LB) Score ___ (RB) | Left bank 10 9 | 8 7 6 | 5 4 3 | 2 1 0 |
|  | Right bank 10 9 | 8 7 6 | 5 4 3 | 2 1 0 |
| Riparian Vegetative Zone Width (score each side of channel. Note: determine left or right side by facing downstream) | Width of naturally vegetated riparian zone >100 feet; human activities, (i.e., parking lots, roadbeds, clear-cuts, lawns, or crops) and grazing have not impacted zone. | Width of riparian zone 50 - 100 ft; human activities and grazing have impacted zone only minimally. | Width of riparian zone 25 - 50 ft.; human activities and grazing have impacted zone a great deal. | Width of riparian zone < 25 feet: little or no riparian vegetation due to human activities. |
| Score ___ (LB) Score ___ (RB) | Left bank 10 9 | 8 7 6 | 5 4 3 | 2 1 0 |
|  | Right bank 10 9 | 8 7 6 | 5 4 3 | 2 1 0 |
| HABITAT SCORE | Sum of score for all 10 categories for stream type (high or low gradient): _________________ x 100 = 200 |

# Text boxes

Comments: